## Slide 1
Digital Audio Compression
Seonkyo Ok

## Slide 2: Goal
reduce size and
minimize quality loss

## Slide 3: Contents Theory Methods Example 01 02 03

## Slide 4: Theory

## Slide 5: Audio Signal

## Slide 6: Characteristic of Sound Waves
determines
pitch
Frequency
determines loudness
Amplitude
determines
characteristic
Timbre

## Slide 7
Pulse
Code
Modulation

## Slide 8: Pulse Code Modulation
Encoding
Quantization
Sampling

## Slide 9: Sampling
Nyquist Theorem
To adequately reproduce a signal,
it should be periodically sampled at a rate
that is twice the highest frequency
of the original signal
“the reduction of a continuous-time signal to a discrete-time signal”
Wikipedia
lowering sampling rate leads to compression

## Slide 10: Quantization
“mapping input values from a large set to output values in a (countable) smaller set”
Wikipedia
larger level distance leads to compression
Human’s perceptual ability is also considered
Notice that quantization induces error,
despite the Nyquist sampling condition

## Slide 11: Encoding
Gray code
Single bit error results in
error of one level of amplitude
except when MSB is erroneous.
“assigns binary numbers to amplitude values”

## Slide 12: Codec
“a device or computer program which encodes or decodes a digital data stream or signal.
a portmanteau of coder-decoder”
Wikipedia
Notes: princeton

## Slide 13: Perceptual Coding ADPCM MDCT
perceptually lossless
adaptive
differential
PCM
modified discrete
cosine transform
Methods

## Slide 14
perceptually lossless
Perceptual Coding

## Slide 15: Perceptual Coding
Not all frequencies are needed
Humans are more sensitive to 2~4 kHz

## Slide 16: Perceptual Coding
loud sound can dominate
temporal masking
after hearing loud audio,
weak audio becomes inaudible
hearing threshold
time resolution

## Slide 17: Companding
“reduce the dynamic range of an audio signal
for better signal-to-noise ratio at lower bit depths”
the loudest tolerable - 120dB
the weakest detectable - 0dB
human cannot perceive
1dB difference which is
12% in amplitude
nonlinear quantization save bits

## Slide 18: A-law / μ-law

## Slide 19
ADPCM

## Slide 20: Differential PCM
can be compressed more if differences are later entropy coded

## Slide 21: Adaptive DPCM
adaptive scale factor in quantization step
adaptive number of bits of difference signal

## Slide 22: MP3
MPEG-1 Audio Layer-3

## Slide 23: Subband Coding
assign more bits
to more sensitive region

## Slide 24: Temporal masking

## Slide 25
MDCT

## Slide 26: Fast Fourier Transform
FFT – O(nlogn)
divide&conquer
“computes the discrete Fourier transform of a sequence”
Wikipedia
converts a signal to a representation in the frequency domain
frequency domain analysis
DFT - O(n2)

## Slide 27: Discrete Cosine Transform
FCT – O(nlogn)
less number of terms are needed to represent a signal
use only real part
better for compression

## Slide 28: Modified DCT
two input blocks at a time
avoid artifacts at block boundaries
used widely in audio compression

## Slide 29: MP3
MPEG-1 Audio Layer-3

## Slide 30
Total loyalty fee for MP3 in ’06
100 million euros

## Slide 31
www.sciencedirect.com/
microscopy.berkeley.edu/
mintnlatte.tistory.com/
watershipdown42.weebly.com/
de.slideshare.net/deepikakamboj946/
web.sonoma.edu/esee/courses/ee442/
References
wiki.gurubee.net/
blog.naver.com/vasurada0/
namu.wiki/
wiki.hydrogenaud.io/
en.wikipedia.org/
www.ktword.co.kr/

## Slide 32
kocw.or.kr/
movavi.io/
www.telecomabc.com/
ece.utexas.edu/
www.dspguide.com/
evive.cc/
ic.ac.uk/
tutorialspoint.com/
www.handelsblatt.com/
cs.stanford.edu/
researchgate.net/
washingtonpost.com/
dsp.stackexchange.com/
www.mp3-tech.org/
References

## Slide 33: THANKS